## Slide 1: Introduction to Computing Memory Architecture Lab.
September 25, 2020
Sungjoo Yoo
Computing Memory Architecture Lab.
CSE, SNU
http://cmalab.snu.ac.kr

## Slide 2: Overview
Prof. Sungjoo Yoo, ’00 PhD SNU
  ~’04 TIMA lab, France
  ~’08 S. LSI, Samsung Electronics (involved in 1st SSD product and iPhone AP design)
  ~’15 POSTECH, ~now SNU
Deep learning design optimization: 5 PhD students
  Low rank approximation [ICLR16]
  Quantization [CVPR17][ECCV18][Arxiv18][ECCV20]
  Hardware accelerator [DATE17][D&T18][TCAD18][ISCA18][Microp20][Access20]
  Self-supervised learning for optimizing mobile neural networks
Deep learning application: 2 PhD students
  Recommender system on server and mobile
  3D understanding models for AR/VR devices
Industrial collaboration
  Facebook, Google, Samsung, Hyundai Motors, SK Hynix, SK Telecom, Naver

## Slide 3: Redundancy in Neural Networks
Redundant filters [LeCun]
AlexNet
Layer | Zero Weight [%] | Zero Activation [%]
conv1 | 15.7 | 0
conv2 | 62.1 | 50.9
conv3 | 65.4 | 76.3
conv4 | 62.8 | 61.8
conv5 | 63.1 | 59.0
Abundant zero values (in AlexNet)
Pruning
ReLU

## Slide 4: Low-rank Approximation in CNN [ICLR16]
128 59
48x5x5  25x5x5
48x5x5

25x5x5
27x27
Y
X
Z
Z’
U3
U4
C
48
55
55
128
27
27
25
59
55
55
27
27
[Kim, ICLR16]

## Slide 5: Results on Galaxy S6
Significant reductions in energy consumption and runtime
  Energy: 4.26X~1.6X
  LPDDR4 and Mali GPU
3.41X
4.26X
1.6X
Galaxy S6 results
[Kim, ICLR16]

## Slide 6: Skipping Zero Values in Both Weight and Act
PE 0
PE 1
Proportional to intersection of non-zero inputs
K: kernel weights
A: input activations
P: partial sums
Cambricon-X
Cnvlutin
Broadcast
Proposed Architecture
Zero-induced load imbalance
*
*
Zero bit-vectors
Zero bit-vectors
[Kim, D&T18]

## Slide 7: 4X~5X Speedup in AlexNet and VGG-16
Chart: Speedup
| Alexnet | VGG-16
WZ | 1.6424 | 1.778
AZ | 2.2408 | 2.5287
WAZ | 3.3404 | 4.1656
WAZ+KA | 3.9962 | 5.2398
AlexNet
4x (AlexNet) and 5.2x (VGG-16) speed up w.r.t. Eyeriss
1.8x (AlexNet) and 2.1x (VGG-16) speed up w.r.t. AZ (Cnvlutin)
19.6% (AlexNet) and 25.8% (VGG-16) speed up w.r.t. WAZ
4x
5.2x
[Kim, D&T18]
Notes: 완성

## Slide 8: Outlier-aware Quantization (OLQuant)
Observation
  Reduced precision suffers from quantization error mainly due to outliers
Proposed idea
  Handle outliers (e.g., 1~3% of total data) separately from the other data
Smaller quantization error for all the data
  Outlier  high precision, e.g., 16 bits, at no quantization error
  Majority of data  reduced precision with narrower region, i.e., smaller quantization error
Weights in 2nd CONV of AlexNet

## Slide 9: Feasibility Test: AlexNet
4-bit quantization with outliers of 0.5% already gives good accuracy
Outliers of 3.5% lose only <1% accuracy
Weights in 2nd CONV of AlexNet

## Slide 10: OLQuant Reduces Memory Cost in Training
9X reduction in stored activations for ResNet-50 training
  3 bits (98%) and 32 bits (2%) for activations
3 bits (98%)
32 bits (2%)
[Park, ECCV18]

## Slide 11: Results: Memory Cost Reduction in Training with Full-Precision Training Accuracy
[Park, ECCV18]

## Slide 12: OLAccel: 4-bit Hardware Accelerator for Outlier-aware Quantization
Basically, 4-bit computation
Consists of PE groups
Each PE group has 16-way SIMD lanes
[Park, ISCA18]

## Slide 13: ResNet-18 without Fine-tuning
Pruned model
8-bit OLAccel vs. ZeNA8
  OLAccel8 gives 29.0% and 49.5% reduction in cycle and energy
16-bit OLAccel vs. ZeNA16
  OLAccel16 gives 25.3% (cycle) and 62.2% (energy) reduction
29.0%
25.3%
49.5%
62.2%
[Park, ISCA18]

## Slide 14: Activation Instability due to Weight Quantization (AIWQ)
In low precision, the same Dw can have larger impact on the activation output, which can make output activation distributions significantly change after weight update

## Slide 15: AIWQ Metric based on KL Divergence
Normal distribution (i.e., 2nd order) model of per-channel output activation before (qt) and after (pt) batch t
AIWQ = Per-layer expectation of channel-level KL divergence between two distributions p and q
[Park, ECCV20]
After weight update
in iteration t
Before weight update, i.e.,
weights in iteration t-1
p
q
layer level instability
channel level

## Slide 16: Incremental Freezing of CONV Weights while Continue to Train the Others
Freeze the weights of 1/3 of the entire layers (having large AIWQ) and train the other CONV weights and BN layers
Freeze the weights of another 1/3 layers and train the other CONV weights and BN layers
Freeze the remaining 1/3 layers (i.e., all CONV weights) and train BN layers
Depthwise
Reduction
Expansion
Freeze 1/3
Freeze 1/3
Freeze 1/3
[Park, ECCV20]

## Slide 17: ImageNet Experiments
Linear quantization of activations/weights on all layers
  including first/last layers
4-bit quantization gives 1.5% top-1 accuracy loss in MobileNet-v3
  8 bits for input pixel data and activation of squeeze-and-excitation
-0.496 %
-0.380 %
-1.484 %
[Park, 2020]

## Slide 18: Overview
Prof. Sungjoo Yoo, ’00 PhD SNU
  ~’04 TIMA lab, France
  ~’08 S. LSI, Samsung Electronics (involved in 1st SSD product and iPhone AP design)
  ~’15 POSTECH, ~now SNU
Deep learning design optimization: 5 PhD students
  Low rank approximation [ICLR16]
  Quantization [CVPR17][ECCV18][Arxiv18][ECCV20]
  Hardware accelerator [DATE17][D&T18][TCAD18][ISCA18][Microp20][Access20]
  Self-supervised learning for optimizing mobile neural networks
Deep learning application: 2 PhD students
  Recommender system on server and mobile
  3D understanding models for AR/VR devices
Industrial collaboration
  Facebook, Google, Samsung, Hyundai Motors, SK Hynix, SK Telecom, Naver

## Slide 19: Visual Localization: Image Retrieval and Pose Estimation (Naver Labs)
https://www.naverlabs.com/storyDetail/173
https://www.naverlabs.com/storyDetail/161

## Slide 20: Naver Labs Localization & Mapping Challenge 2020/4-8
Indoor dataset: Pangyo Hyundai department (B1, F1)
Outdoor dataset: Pangyo and Youido
https://www.naverlabs.com/storyDetail/161
ㅇ
ㅇ
.
.
Database
Global
Descriptor
Image Retrieval
Feature Matching & Re-ranking
Lidar Projection & 2D-3D matching
Pose Estimation
DB cluster
Query
ㅇ

## Slide 21: Related Work: Facebook’s Live Map
Live map consists of 3 layers
  Content, index and location
It allows an avatar to be placed in our world (in AR/VR) in a natural way
It also helps mobile AR/VR devices save energy since those devices do not need to sense everything around us every time
Instead, they can focus on dynamic differences from the live map, which reduces computation cost
https://www.facebook.com/facebookrealitylabs/videos/357103208754306

## Slide 22: Related Work: Facebook’s Project Aria
Especially, wearable devices will offer ego-centric view
In Project Aria, they use smart glasses, a research prototype, to collect ego-centric data
https://www.facebook.com/facebookrealitylabs/videos/357103208754306

## Slide 23: Research Plan Towards Powerful Mobile AR/VR Devices
“Need 10X~100X energy efficiency improvements and Privacy”
  Vikas Chandra, Facebook Reality Lab. (HENP 2020 Workshop)
Algorithm optimization
  On-device self-supervised learning
  Exploiting multi-modality, e.g., depth sensor, image, voice, motion, …
Compiler-level optimization
  AutoML for binary neural network
  Low-precision on-device training
Hardware optimization
  Efficient accelerator for binary neural networks and training/programmability
  In-memory computation for conditional execution of extremely large binary neural network

## Slide 24: Thank You!
sungjoo.yoo@gmail.com